## Slide 1: Parity Bit Checker Bit Stuffing Byte Stuffing
Name:Yadav Rohit Krishna Kumar
Branch:CE_C3_137
Enroll No:22002170110210

## Slide 2: Parity Bit Checker
An additional bit (0 or 1) added to data to make the number of 1s either even (even parity) or odd (odd parity).
The receiver checks the parity to detect errors.
Data =1010110,Even parity->10101101

## Slide 3: Destuffing Stuffing Bit Stuffing
The reverse process of bit stuffing
Remove the 0 inserted after five consecutive 1 s during transmission
011111010110 ->01111110110
In communication ,flags are used to mark the start and end of a frame
Like 01111110
To avoid confusion when data contains the same flag,a 0 is inserted after every five consecutive 1 s

## Slide 4: Destuffing Stuffing Byte Stuffing
The receiver looks for the escape byte
When the escape byte is found, it removes the escape byte and interprets the next byte as part of the original data.
Byte Stuffing is a data-link layer technique used in data communication to ensure that control characters (like start-of-frame, end-of-frame, or escape characters) are not confused with data

## Slide 5: Parity Bit 01 Bit Stuffing 02 Byte Stuffing 03 Applications
Found in RAM, communication protocols, and storage systems.
Used in HDLC and CAN bus protocols.
Found in PPP and Ethernet.
Thanks!

## Slide 6: Thanks!
Please keep this slide for attribution